## Slide 1
SAFEX Webinar N° 6 MANAGEMENT OF CHANGE
April 9th, 2024
America & Europe – 09:00-11:00 Cleveland Time
Asia & Pacific – 18:00-20:00 Cleveland Time
Hosted by EPC Groupe, chaired by Thierry Rousse
With a special WG dedicated to MOC including:
Dawn Goosen, Nadia Engler, Diana Lazarte, Johanne Dellarovere
Paulo Siqueira, Joao Roorda, Joseph Sindane, Bob Woolley

## Slide 2: introduction
1

## Slide 3
INTRODUCTION

## Slide 4
INTRODUCTION
Notes: Team: key success
New Format for this second session
Best solution will be our solution

## Slide 5
WORK GROUP MEMBERS
Bob Wolley
Nadia Engler
João Roorda
Diana Lazarte
Paulo Siqueira
Thierry Rousse
Dawn Goosen
Joseph Sindane
Johanne Della Rovere
Notes: A special WG dedicated: Team effort
New Format for this second session
Innovative
Passion
Diversity

## Slide 6
AGENDA
1
2
3
4
INTRODUCTION
MANAGEMENT OF CHANGE – CONCEPT , TYPES AND HOW TO SUCCEED
GROUP ACTIVITY & FEEDBACK
DISCUSSION & CLOSURE
5 min
25 min
60 min
20 min
Notes: Introduction - 5 mn- Thierry
Presentation - 25 Minutes - Dawn
Instructions for exercise – 5 Minutes Joao
Exercises - 30 Minutes – 5 leaders/ Facilitators
Feedback (only highlights!) - 35 Minutes – Each Facilitator
Discussion & wrap up - 20 Minutes - Bob
Closure

## Slide 7: Management of change
2
What do we mean by change?
How do we succeed at Management of Change?
Why is Management of Change important?

## Slide 8
MANAGEMENT OF CHANGE
Equipment
Design / Drawings
Infrastructure
Operational / Process
Procedures / Standards
Organisational / People
Raw Materials / Suppliers
Product
Software
Contractors
Excluding the replacement of a plant hardware component which, in the professional judgement of a qualified engineer, is of an identical or equivalent specification to that which has been removed.
Changes may be permanent or temporary and related to:
A change is defined as any alteration that can result in deviation to any part of plant & equipment , process, methods/ procedures, specifications, transport routings, waste/ emissions (not an inclusive list)
What do we mean by change?

## Slide 9
OPERATING REALITY
Changes will be made to the process
Improve productivity & efficiency
Keep up with industry standards and requirements
Rectifying design issues/ equipment/ process problem
Improve safety
Reduce health & environmental impact

## Slide 10
OPERATING REALITY
What keeps us from recognizing change?
Pressure to perform
Going too fast
Lack of knowledge
Never happened before
Been doing it forever

## Slide 11
MANAGEMENT OF CHANGE
80% of large-scale accidents in process industry can be traced back to improperly managed change.
Management of change process ensures change does not inadvertently introduce new risk or hazards.
CHANGE = RISK
Why is Management of Change important?

## Slide 12
April 2nd, 2010
PETN Dryer building before and after decomposition reaction lead to detonation of PETN, leaving a 3.5 m deep crater.
Change to external supplier not fully considered. 1st batch of PETN – drying started before quality release was issued.
INCIDENT EXAMPLES
March 9th, 2022
Explosion took place on the main evaporator of the acetic acid distillation system next to HMX plant (10 kg explosive material)
Changes to the installation and procedure did not follow a formal process (HAZOP, MOC).

## Slide 13
INCIDENT EXAMPLES
January 14th, 2021
During the standard procedure of burning waste cartridged emulsion explosives there was an explosion (160 kg cartridged emulsion explosives).
Changes to the quantity of explosive waste being burned.
July 29th, 2004
Maintenance contractor checking engine oil level on MMU was fatally injured when another MMU impacted the MMU he was working on.
Change in layout leaded to more congestion and insufficient space to turn and exit.

## Slide 14
MANAGEMENT OF CHANGE
Management of change needs to be formally:
Documented
Reviewed
Approved
Implemented
Implement a Management of Change process / system that everybody will use.
Implement consistent business rules and checklists.
Ensure stakeholder involvement and risks assesment of all changes.
Ensure all tasks required to manage the change are completed before introducing the change.
Make sure temporary changes do not become permanent without oversight or confirmation evaluation of permanent change.
How do we succeed at Management of Change?

## Slide 15
MOC PROCESS
15
REQUEST FOR CHANGE
CHANGE ANALYSIS /
RISK ASSESSMENT
CHANGE APPROVAL / REJECTION
CHANGE IMPLEMENTATION & SHE ACCEPTANCE
CHANGE COMPLETION
Description of the proposed change.
Proposal is analyzed/ assesed by personnel with knowledge, skill , training and experience to identify hazards, assess risk, and determine controls associated with proposed change.
Approval by Manager with operational control of the process where the change will be implemented.
All controls in place and change is as intended before change is made operational.
Complete all tasks related to the change and verify the objective of the change was achieved.

## Slide 16
ROLES AND RESPONSABILITIES
16
Initiator
Owner
Reviewer
Approver
Implementers
Trained and Authorised person, who defines the change request and initiates the change.
Ensures all process steps for management of change are adhered to and requirements are met before implementation and change is appropriately communicated.
* May also be the initiator and implementer.
Review the information supplied and act as area subject matter experts
Approve the change to start implementation. Manager of the area where change is being implemented.
Execute authorised and approved changes or modifications.
BUSINESS MANAGER: ENSURES MANAGEMENT OF CHANGE SYSTEMS ARE IN PLACE AND USED.

## Slide 17
DOCUMENTATION
17
Change Register
Defines the scope and details of the change.
Explains reasons or justification for the change.
Provides traceability for the analysis and approval process.
Formal review and approval is required.
Demonstrate that change has been considered by appropriate people and that is has been agreed that it is safe to continue its implementation.
Reviewers and Approvers must be qualified and include affected people.
E.g. Relevant Line managers, SHES representatives, Responsible engineers, Operators, Quality representatives, Legal Counselors, etc.
Review and Approval
Change Identification Checklists
Equipment
Organisational Issues
Changes to materials of construction
Changes to rates or corrosion or erosion
Changes to potential for foreign objects
Changes to arrangements to secure fasteners
Changes to potential for concealed energetic materials
Changes to inspection or maintenance requirements
Changes to design pressure or temperature of equipment
Changes to skill and competency of the people to complete the task safely.
Changes to job functions performed by individuals
Changes to position descriptions / additional responsibilities
Changes to the number of people required to safely perform tasks
Changes to the likelihood of critical errors.
Changes to availability of supervisory resources
Changes to work hours or shift arrangements Changes to communication between individuals or workgroups Changes to selection criteria for new recruits or transfers

## Slide 18
SUMMARY
Uncontrolled change leads to safety issues/ incidents, incorrect purchases, costly downtime and rework.
Lack of Management of Change Systems has been identified as the cause of many incidents, accidents and fatalities in the industry.
Change needs to be critically considered for potential to introduce new or change current risk level
Change must be formally documented , registered, reviewed and approved prior to implementation
Everyone is responsible to ensure any change within their work area is managed though our Management of Change System / Process

## Slide 19: GROUP ACTIVITY & fEEDBACK
3

## Slide 20
INSTRUCTIONS
For this Webinar, we will split the attendees in rooms for the group activity:
Each room will have a leader and a facilitator:
Leader: Will Ensure the meeting is working properly. more on the “tech” side of things.
Co Leader: Will drive the discussion and provide feedback about the discussion later on.
For each group, there is a MOC case for discussing:
What should have been done differently?
What makes this case special?
Return to the main meeting and share feedback.
Notes: 1 – Supplier or other: Nadia / Martin, AUSTIN Study Case N°1
2 – Raw Material: Dawn / Diana, ORICA Study Case N°1
3 – Raw material or other: Joao / Paulo, looking for a case
4 – Equipment: Thierry / Johanne, EPC Study Case
5 – Organization: Bob / Rob Chapman, EPC Study Case

## Slide 21
CASE N°1 – FEEDBACK
Incident description & impact
Lead Azide Dust Explosion
What went wrong?
The building where this incident occurred is comprised of three individual bays where lead azide and/or PETN is brought in wetted and then washed with alcohol and dried in a heated bowl.
A detonation occurred inside an extractor of the washing and drying lead azide bay.
Impacts:
No injuries occurred as a result of this event.
Damage to extractor and false wall
Shrapnel impact to Barricade
Change:
However, at some point it was replaced with a different model. Replacement unit was similar in appearance but over time it accumulated explosive dust/residues inside.
Friction between impeller and housing initiated the detonation, the replacement model was similar in appearance but not rated for hazardous environments.
Documentation of when the replacement took place is unknown.
Extractors were not part of a preventive maintenance program.
Rather than placing orders to maintain spare parts, units were substituted out from a different process.
Nadia & Martin
Notes: 2 – Raw Material: Dawn / Diana, ORICA Study Case N°1

## Slide 22
CASE N°2 – FEEDBACK
Incident description & impact
Booster Fire incident at Minden , Louisiana - March 2011
What went wrong?
At ~ 07h20 on 21 March 2011 a pouring operator removed booster trolley from cooling oven and noticed that two of the boosters were emitting smoke.
Operator immediately activated the emergency evacuation of the plant – fire engulfed building 927 at ~ 07h25 am. The fire burned for approximately 3 hours with no detonation and no injuries.
Impacts:
Challenges in removal of solidified Pentolite from kettles in second production house.
Production plant was down for recovery and rebuild for 6 months
Change:
Boosters that were smoking were first boosters poured using new degrading agent tablet.
Organization failure to anticipate the potential runaway reaction with new DA.
Failure to follow existing procedures, e.g. apply management of change process.
Flawed assumption that analytical testing methods will generate equivalent results for all degradable systems to be tested.
Dawn & Diana
Notes: 2 – Raw Material: Dawn / Diana, ORICA Study Case N°1

## Slide 23
CASE N°3 – FEEDBACK
Explosion of a ANSOL Pump
Incident description & impact
What went wrong?
A Bulk Emulsion production plant operator noticed a leak in an ANSOL (ammonium nitrate solution) transfer pump.
The mechanic’s examination pointed to excessive wear of the gasket. He found a replacement gasket that fit and replaced the damaged one – operation was back up and running.
Three hours later the pump exploded.
Impacts:
The centrifugate pump used to transfer ANSOL exploded.
There were no injuries
The plant stopped production.
Change:
Replacing the original Teflon gasket with a graphite one.
Failure in the MOC system and to assess the risks of the change.
  Failure in the MOC training of the operator and mechanic.
  Absence of original spare parts for pump maintenance .
  Lack of BOS knowledge by the operator and mechanic.
João & Paulo
Notes: 3 – Raw material or other: Joao / Paulo, looking for a case

## Slide 24
CASE N°4 – FEEDBACK
Incident description & impact
What went wrong?
At the end of a production run, a popping noise was heard from the matrix pump (progressive cavity pump). The operator immediately stopped production and alerted his superiors.
On dismantling, it was found that a retaining pin between the connecting rod and the rotor was badly damaged.
Impacts:
Significant damage on the pump
Change:
The process temperature had to be increased following the use of an aqueous phase with a higher concentration of ammonium nitrate, resulting in an increase in the crystallisation temperature from 72°C to 80°C.
Higher concentration of ammonium nitrate was used in other plants; however bellows had been replaced by nitrile ones. In Belgium the bellows were made of Hypalon.
The change was considered not significant
Johanne & Thierry
Abnormal pump damage
Notes: 4.- Equipment: Thierry / Johanne, EPC Study Case

## Slide 25
CASE N°5 – FEEDBACK
Incident description & impact
What went wrong?
ISO tank full of concentrated nitric acid was positioned on the discharge point and prepared for offload.
When the valve was opened, nitric acid leaked from one of the connections. No attempt was made to close the valve or dilute the acid. Nitric acid made contact with the tires of the trailer and started a fire.
Impacts:
There were no injuries but there was major asset damage by the leak and fire.
3 weeks loss of production.
Investigation by the regulators.
Change:
The task of connecting the tanker changed from plant operators to tanker drivers.
Numerous changes in management and personnel over the preceding years.
Failure to properly manage creeping change including: Personnel and competence, Techniques, Equipment and Suppliers.
Procedure was not standardised
Inadequate immediate response
Robert & Marion
Nitric acid leak and fire
Notes: 2 – Raw Material: Dawn / Diana, ORICA Study Case N°1

## Slide 26: DISCUSSION & CLOSURE
4

## Slide 27
DISCUSSION & CLOSURE
SAFEX MoC Webinars
  November 2023
  April 2024
Next Steps
  Management of Change e-Learning Module
  Any other ideas? You can be a part of this journey!
Help us improve!
https://forms.office.com/r/W4vaV40Sma

## Slide 28
DISCUSSION & CLOSURE
SAFEX MoC Webinars
  November 2023
  April 2024
Next Steps
  Management of Change e-Learning Module
  Any other ideas? You can be a part of this journey!
Help us improve!
https://forms.office.com/r/w3fnHhE02E​

## Slide 29
SAFEX Webinar N° 6 MANAGEMENT OF CHANGE
Thank you for your participation!
Hosted by EPC Groupe, chaired by Thierry Rousse
With a special WG dedicated to MOC including:
Dawn Goosen, Nadia Engler, Diana Lazarte, Johanne Dellarovere
Paulo Siqueira, Joao Roorda, Joseph Sindane, Bob Woolley